## Slide 1: Music signal processing
COMP.SGN.120
Introduction to Audio processing
Lecture 12

## Slide 2: Music
Music is one of the richest and most carefully constructed audio signals.
  Music has several overlapping and simultaneously active sources.
  Prominent structures are organized in both time and frequency.
Music waveform carries more information than most other signals
In this course, we don’t assume prior knowledge of music.
Basic concepts required by the automatic processing methods are explained.

## Slide 3: Music representation
Music has its own written notation (musical score)
  Describes musical work with formal language based of musical symbols and letters
  Musician can create a performance by following such instructions
  Similar to different languages, one needs to study this language to master it.
Sheet music representation
  Visual description of a musical score.
  Image format.
  Guide for performing music.
Duration of the notes
Parts of a note
Staff

## Slide 4: Music representation
Symbolic representations
  Description based on entities with explicit musical meaning.
  Given in digital format that can be parsed by a computer.
  MIDI (Musical Instrument Digital Interface) representation.
Audio representation
  Physical description
  Encoding of sound wave
Piano roll

## Slide 5: Musical score or Sheet music
Instruments such as the violin, or a singer, can produce notes with arbitrary pitch values
These are quantized into notes
By reading the sheet music, a musician can create a performance:
Figure: staff (5 lines, 4 spaces) denote pitch
  Pitch raises upwards
Time goes from left to right
The clef at the start of the staff indicates the position of a particular note on the staff.
Perceptual property that allows a listener to order a sound on a frequency related scale.
- Musical symbol (score representation)
- Pitched sound (audio representation)

## Slide 6: Western music notation
The standard Western music notation is based on a staff.
Generally, it begins with a clef symbol, which indicates the position of one particular note on the staff.
Treble clef or G-clef
Bass clef or F-clef
Also timing of notes is quantized. (Whole note, quarter note, one-eigth, etc.)
  Denoted with different shapes of note symbols (or additional symbols)
The overall tempo and style of the piece can be specified by textual notations
Allegro con brio (fast with vigor and spirit)
Andante con moto (moderate tempo with motion)

## Slide 7: Music scales
Pentatonic (5 notes)
Major and minor diatonic (7 notes)
Chromatic (12 notes)
The white keys are the natural notes
Black keys are named using sharps or flats

## Slide 8: Music terms
Western music uses log-scale with 12 notes in each octave range
  Notes are one semitone apart
  Called twelve-tone equal-tempered scale
Nominal F0 of note n is 440*2(n/12) (Hz)
  440 Hz is an agreed anchor point
  Index n varies from -48 to 39 on a standard piano keyboard
Notes in each octave are lettered:
  C,C#,D,D#,E,F,G,G#,A,A#,B
  The pound symbol (#), read as “sharp”, increases pitch of a note by one semitone
The octave range is indicated with a number following the letter.
  By convention: A4 = 440 Hz
  E.g. A4# = 466.16 Hz, A5#=932,3 Hz
https://pages.mtu.edu/~suits/notefreqs.html
Piano
violin

## Slide 9: Music terms
Inter-onset interval (IOI)
  Time interval between beginning of two sounds
  Defines the rhythmic characteristic of a melody
  Although duration plays a role too, the lOIs are more crucial in determining the perceived rhythm
  Rhythmically important instruments (e.g. drums) produce exponentially decaying waveshapes without a unique definition of duration.
Melody
  Series of pitched sounds with musically meaningful pitch and IOI relationships
  e.g. sequence of written notes
Chord
  A combination of three or more simultaneous notes

## Slide 10: Constant Q transform

## Slide 11: STFT Spectrogram re-cap
Spectrum estimated in short consecutive frames
  Windowing to avoid spectral blurring
Transient-like sounds are difficult to represent and process in the frequency domain
  Results in time blurring
Notes: brent .wav

## Slide 12: Spectrogram as music notation
Spectrograms look like sort of musical notation. However, the low frequencies are squish together at the bottom, while far a part at the top.
Music notation is in logarithm scale
Linear scale
Logarithmic scale
Mel scale
We want more accuracy at the lower frequencies and less accuracy in the highest frequencies

## Slide 13: Constant Q transform
Related to Fourier transform.
Time-frequency representation where the frequency bins are uniformly distributed in log-frequency and their Q-factors (ratios of center frequencies to bandwidths) are all equal
This transform is very well suited for musical data, because the output is effectively amplitude against log frequency, so it needs less bins to cover a given range.
It also mirrors the human auditory system where at lower frequencies the resolution is better.

## Slide 14: Constant Q transform
Initially proposed in the late 1970s.
Modifies the STFT such that the frequency bins are logarithmically spaced.
The windowing function is adjusted with center frequency so that the width of each bin increases in proportion to the center frequency.
The ratio of frequency-to-bandwidth is kept constant, hence the term “Constant-Q”.
Computationally complex and difficult to implement technique in a real-time music context.

## Slide 15: Constant Q transform
It can be thought of as a series of logarithmically spaced filters, with geometrically spaced center frequencies.
number of filters per octave.
k – filter index
This yields to a constant ratio resolution of
Octave is a musical interval.
  Distance between one note and the next note bearing its same name.
  Distance between one note and another note that is double its frequency.
  A4 (440Hz) and A5 (880Hz)

## Slide 16: Constant Q transform
Mathematical definition:
where N is length of input signal, gk(m) is zero-centered window function that picks one time frame of the signal at point n and fs sample rate
Compare CQT with short-time Fourier transform (STFT):
where now the window function h(m) is the same for all frequency bins
In CQT, the center frequencies are geometrically spaced: fk=f02k/B where B determines the number of bins per octave and f0 is lowest bin
In DFT, the center frequencies are linearly spaced: fk =kfresolution

## Slide 17: Constant Q filters
The constant Q Transform compared to FFT is quite similar, except that the window function in FFT is the same for all frequency bins, while in CQT we have different windows
The center frequencies for the bins are spaced geometrically for the CQT, and linearly for the DFT.
The higher the frequency the larger the bandwidth of the filter, they accept more variance in the frequency that has been given as input.

## Slide 18: Constant Q transform illustrated
Time-frequency resolution ofered by the constant Q transform.
Long window in time for the lower frequencies and obtain a good frequency resolution, and viceversa.
At higher frequencies we have worse frequency resolution but very good temporal one.
Y-axis is log-frequency, therefore the bandwidths are actually EQUAL on log-scale

## Slide 19: Computing CQT
Efficient computation achieved by:
1. FFT of the entire input signal
2. Apply one CQT frequency-bin wide bandpass on the (huge) spectrum
3. Move subband around zero
4. Inverse-FFT transform the narrowband spectrum to get CQT coefficients over time for that bin
Schörkhuber, C., Klapuri, N. Holighaus, and M. Döfler, "A Matlab Toolbox for Efficient Perfect Reconstruction Time-Frequency Transforms with Log-Frequency Resolution," AES 53rd International Conference on Semantic Audio, London, UK, 2014.
https://www.cs.tut.fi/sgn/arg/CQT/
librosa.core.cqt

## Slide 20: CQT vs STFT
STFT, search of a trade off.
So here we have good resolution for the low frequencies (upper panel)
While in the panel below we have better resolution for the higher ones.

## Slide 21
Another example of constant Q transform representation

## Slide 22: Drawbacks of CQT
CQT is computationally more intensive than DFT spectrogram
CQT produces a data structure that is more difficult to handle than the time-frequency matrix (spectrogram)
The spectrogram is simply a time-frequency matrix, while in CQT we need to handle coefficients that represent different lengths.
This is because in CQT the time resolution varies for different frequency bins, in effect meaning that the “sampling” of different frequency bins is not synchronized.

## Slide 23: Example application: Pitch shifting
Pitch shifting is a natural operation in CQT domain:
1. CQT
2. Shift CQT coefficients
3. Retain phase coherence
4. Inverse CQT
Examples:
Original
- 6 semitones
+6 semitones
Transients at high freqs. are retained due to short frame
phase coherence is lost when CQT coefficients are shifted along the frequency dimension.
Neighboring bins excited by the
same sinusoid share the same phase value
Notes: Orig, p6 m6 3 examples

## Slide 24: Chroma

## Slide 25: Chromatic scale
The term chromatic is derived from the Greek word chroma, meaning color.
In music domain it relates to the twelve different pitch classes.
  Notes C2 and C5 both have the same chroma value C.
All notes that have the same chroma value belong to the same pitch class.
m
Chroma representation gives a description of the different notes present in the audio without distinguishing the octave in which they occur.
Chromatic circle
Shepard’s helix of pitch, represents the linear pitch space as a helix wrapped around a cylinder. The octave-related pitches lie along a vertical line.
(From slide 8)
Music scales:
Chromatic (12 notes)

## Slide 26: Chromagram
The main idea of chroma features is to aggregate all spectral information that relates to a given pitch class into a single coefficient
Basic algorithm using FFT
C4 12*log2(261.5/261.5)=0
C#4/Db4 12*log2(277.18/261.5)=1
D4 12*log2(293.66/261.5)=2
for each fft_bin do
chroma_bin = mod(round(12*log2(freq(fft_bin)/freq(C4)) ),12)
chroma_energy[chroma_bin] += fft_energy[fft_bin]
end for
freq(fft_bin): returns the frequency of fft_bin in Hz.
freq(C4): 261.5 Hz
chroma_energy is normalized to retain only pitch info and remove signal level information
The frequency resolution of lower bins and non-tonal energy cause issues, which refined algorithms mitigate

## Slide 27
Piano keys representing the chromatic scale
Magnitude spectrogram
Pitch-based log-frequency spectrogram
Chromagram
Note C3 (p=48) played at time 30 seconds
(MIDI note number)

## Slide 28: Example: Piano notes in different octaves
Notes C0-C3, D0-D3,E0-E3,F0-F3 are played in a sequence
Top figure: power spectrogram of the signal.
  Note the octave raise.
Chromagram shows the same pitch class value for the different octave notes
  Bottom figure evaluated from data using Python/librosa.
Notes: piano

## Slide 29: Example: Chromagram of a chord
C-major (G,E,C), visible in chromagram
Notes: c-major-chord.wav

## Slide 30: Example: Finnish Eurovision 2018 candidate song Monsters by Saara Aalto

## Slide 31: Dynamic Time Warping
Music synchronization

## Slide 32: Music synchronization
Synchronization here refers to a procedure to determine the corresponding position in a piece of music, given another (slightly differently interpreted) piece of music
Figure: Two different tempo performances of a same song

## Slide 33: Music synchronization
Procedure for music synchronization
Uses
  Allows synchronization of score of music with audio track
  Jump to audio position, based on selected score position
  Seamless switching between different versions of same music
  Measure differences in tempo between same musical piece versions
    To analyze the performance

## Slide 34: Music synchronization
Need right types of features that
  Retain relevant information, while suppressing irrelevant details
  Capture similarity between notes and chords
  Allow variation between instrumentation (timbre), tempo, rhythm
  Suitable features include chroma vectors
Dynamic time warping (DTW)
  Used to align the two feature representation sequences (of feature vectors) of two different versions of the same piece of music
  DTW Goal: find an optimal alignment between two sequences
  DTW is used in data mining, information retrieval, and bioinformatics

## Slide 35: Dynamic time warping
Input: two sequences 𝑿= [𝒙1, .. 𝒙N] and 𝙔=[𝒚1,..., 𝒚M]
Define a real-valued cost matrix
is a cost function:
Cosine distance
Euclidean distance
Generally: if 𝒙n is similar to 𝒚n then the cost should be low
A warping path P = (𝒑1, .. 𝒑L) of length L,
  𝒑l=(nl, ml) denotes correspondence between the two sequences
  Starts from 𝒑1=(1,1) and ends in 𝒑1=(N,M)
  Steps are monotonically increasing (no going back in time)

## Slide 36: Example
X=[1,1,0,2,2], N=5, and Y=[1,0,2], M=3
Cost function c(n,m)=|xn-ym|, i.e. absolute distance (L1)
2 | 1 | 2 | 0
2 | 1 | 2 | 0
0 | 1 | 0 | 2
1 | 0 | 1 | 1
1 | 0 | 1 | 1
 | 1 | 0 | 2
2 | 3 | 4 | 0
2 | 2 | 2 | 0
0 | 1 | 0 | 2
1 | 0 | 1 | 2
1 | 0 | 1 | 2
 | 1 | 0 | 2
Optimal path
P* = {(3,5),(3,4),(2,3),(1,2),(1,1)}, L=5
Cost of path: (sum the optimal path cell values (blue)) = 0
Cost matrix
Accumulated cost matrix
Original cost + min(steps) of already computed values.
1 + min(1,1,2) = 1 + 1 = 2

## Slide 37: Example: Music synchronization
A song is sung twice, upper one is 7% faster
Bottom figure: Chroma features (using librosa)

## Slide 38: Cost matrix and optimal path
Distance: Euclidean distance between chromagram vectors at each time instant
Red-lines: Two synchronized notes
Yellow line: Linear time
White line: Optimal path
Optimal path shows the corresponding time instant for both songs.

## Slide 39: DTW summary
Gives the synchronization of feature representations of two signals.
Cost functions
Cosine distance: not sensitive to absolute level (since the vectors are normalized by definition)
Euclidean distance: Is sensitive to level differences if features are not normalized.
Feature normalization: by normalizing the feature vector of each time-value, the feature is not sensitive to level anymore.
Tools: DTW available in librosa
Representation of Euclidean distance (d) and cosine similarity (θ)

## Slide 40: Tempo, beat

## Slide 41: Temporal structure
Music is organized into temporal units, called beats
  Rhythm refers to pattern of strong and weak beats
  Musical meter refers to the rhythm aspect of music
Most noticeable metrical level is the tactus
  Sometimes called “the foot tapping rate” or just “beat”
  Beat is the backbone of a piece of music, which makes the automatic detection of beat an important sub-task in music processing.
  Duration of a beat is given by tempo, indicated in beats per minute (BPM).

## Slide 42: Tempo analysis
Above the level of chords and notes, are phrases and sections
  Coherent sequences of chords/notes that often repeat with no or little variation, e.g. in pop songs: intro-verse-chorus-verse-chorus…
The extraction of tempo and beat is challenging, particularly for music with weak note onsets and local tempo changes.
Tatum (temporal atom) level refers to the fastest repetition rate of musically meaningul accents occurring in the signal.

## Slide 43: Beat tracking
Beat position approximations:
  Often occurs at note onset position
  Intervals are approximately constant
Typical onset detection flow
Onset detection: detect note start time
  For single notes, simply looking at the signal energy is a start
  However, simultaneous occurrence of events makes this approach not so robust, therefore time-frequency domain is more suitable
  Often, temporally simultaneous events do not overlap in frequency.
Signal
Features
Novelty function
Beat positions
Derivative
Peak picking

## Slide 44
Novelty function: find local changes in signal properties such as energy or spectral content.
Fourier tempogram, time –tempo representations, which captures the local tempo characteristics of music signals
Correlation of novelty function and various analyzing windowed sinusoids.
(e)
(d)
(c)

## Slide 45: Beat tracking
The spectral based novelty function for beat tracking:
Take STFT X(n,k) of signal x(t)
n=time frame, k=frequency index, t=sample time index
Apply log-compression to magnitude spectrum:
where 𝛾 = 1 weak components become visible
𝛾 >> 1: may amplify also noise-like weak components
Calculate the spectral novelty function:
Pick peak locations of ∆(n) and convert STFT time frame index n into seconds.
Signal
Features
Novelty function
Beat positions
Derivative
Peak picking

## Slide 46: Example: Queen Another one bites the dust
Double bass note (offbeat)

## Slide 47: Tempo analysis
Tempo = how many times per minute the beat repeats?
Tempo = 60 / T [BPM],
  where T is “beat interval time”, BPM is beats per minute
Tempo is extracted by analyzing the periodic behavior of the novelty function.
  Tempo can change during song, so analysis is done in segments of 4-12 s
  Practically we can limit tempo between [30,600] BPM
T (beat interval)

## Slide 48: Music structure analysis

## Slide 49: Structure detection
Self-similarity of temporal segments can be examined using a similarity matrix, with cells representing similarity of two feature vectors 𝒙n, 𝒙m from time instantants n,m
  e.g. cosine similarity:
  Idea: similar vectors 𝒙n, 𝒙m should lead to high similarity value.
Recurring patterns become visible as large values
  Homogeneity results in a block structure (features capture musical sequences that stay somewhat constant over the part)
  Two repeating harmonic progressions or melodies highly similar to each other create diagonal lines in the self-similarity matrix.

## Slide 50: Structure with self-similarity matrix
Similarity measure: cosine.
Features: chroma.
Each cell is the cosine-distance between the chroma vectors in x,y coordinate time positions of same signal.
Repeated patterns are similar (high cosine similarity) and show as diagonal strips
D & F are most similar:
  chorus (song+accompaniment)
C is similar to D and F, visible as elevated value block structure, less diagonal stripes:
  It is the chorus without singer
B has diagonal stripes as D and F.
  Chorus with singing and only some instruments present)

## Slide 51: Similarity matrix computation

## Slide 52: Self-similarity matrix
Self-similarity matrix can be used to analyze the structure of a song
Applications
  Automatic segmentation
    Here the lines between song parts were drawn manually, but this can be automatically done
  Audio thumbnailing:
    Extracting most representative part of a song
Tools: Music Structure Analysis Framework
  https://github.com/urinieto/msaf (contains automatic segmentation)

## Slide 53: Content-based music retrieval

## Slide 54: Music information retrieval (MIR)
Multidisciplinary science of retrieving information from music
  Aims to develop strategies to quickly access music collections through content analysis.
Subtasks of MIR include (but are not limited to):
  Beat tracking: Automatic analysis of temporal structure of music (beat, tempo, rhythm, meter)
  Chord and key recognition
  Melody estimation: Melody is a strong indicator of the identity of a musical piece.
  Music fingerprinting (for exact identification of a musical piece)
  Genre recognition
  Recommendation
  Instrument recognition
  Score alignment (synchronize audio and score)
  Structure analysis (which parts are in the song and in what order, intro, chorus, verse)
  ….

## Slide 55: MIR
Information Retrieval
In the general sense, is the task of organizing information and making it accessible and useful.
Process:
  User specifies his/her needs with a query.
  Retrieval system deliver items that are related to the query.
Most systems rely on metadata and textual annotations of the audio content.
Metadata describes the content of the musical piece
  Can be analyzed by humans (domain experts) or by computers
  Factual metadata such as performer, year, name of the song, album.
  Cultural metadata includes attributes like mood, emotion, genre, style, etc.. (Referred also as “tags”)

## Slide 56: Music recommendation systems

## Slide 57: Audio-based music retrieval
Collaborative filtering (CF) does not solve it all
  CF does not allow separating the various dimensions of music similarity, but these are all mixed in the piece profile
  CF alone is not able to deal with items that are new or do not have many listeners
Audio-based MIR addresses the above problems
  Enables “truly musical queries” with specific musical criteria, such as requesting pieces with certain vocal characteristics or slow tempo  profile of a song
  Can be employed even on media libraries that do not have any audience of listeners
On the other hand, audio-based MIR alone cannot measure aspects like quality, usage (popularity), or culture
  The two approaches are complementary
Genre (jazz, rock) tempo (slow, fast)

## Slide 58: Content-based audio retrieval
Content based retrieval make use or the raw music data, rather than rely on manually generated information
Content based music description allows:
  Identify what the user is searching, even if the user does not specifically know herself (music similarities)
  Identify music captured from loudspeakers in a noisy space (e.g. shazam)
  Identify song name based on user’s humming (Query by humming)
Content based retrieval
  Retrieval process starts with a query (text, audio)
  Retrieval system returns all items that are somehow related to the query

## Slide 59: Query mechanisms
Query by example
  Given music representation or fragment, retrieve music with similar parts or aspects.
Browse by similarity
  Find similar music
Query by humming or tapping
Tempo
Lyrics
Music categories (genre, mood, tags)

## Slide 60: Query by humming
Consists of two main steps:
  Melody transcription of a hummed or sung query into a suitable higher-level representation
  Matching that representation against a large database of known reference items
Example method [Ryynänen, M., & Klapuri, A. (ICASSP 2008)]
  Preprocessing: extract melodies automatically from music pieces
  Transcribe the query
Match by Euclidean distance between the two melodic contours (allow time scaling)
Process:
SFTF of the audio
Pitch detection, most dominant pitch tract
MIDI representation (quantize notes)
Encodes in an invariant scaling form
Performed for the whole dataset.
Query 1
First retrieve
Second retrieve
Query 2
First retrieve
Second retrieve

## Slide 61: Music similarity
Music similarity estimation enables query by example and browsing by artist similarity
Widely used acoustic features
  Mel-frequency cepstral coefficients (MFCCs)  timbre/instrumentation
  Chroma: collapse spectral content into one octave and use 12 bins for the total spectral energy on each pitch class (c, c#, d,...,b)  harmonic content
  Rhythmogram (or, fluctuation patterns): cosine transform in blocks that extend in time direction  rhythm

## Slide 62: Features define “similarity”
“Similarity” as such is not well-defined
Is Bohemian Rhapsody by Queen
more similar to … ?
  Bohemian Rhapsody by London Symphony Orchestra
  Killer Queen by Queen
The riddle is solved by choosing the acoustic features
  chroma a) is more similar (composition)
  MFCCs b) is more similar (instrumentation)
User may wish to specify the features when doing query by example

## Slide 63: Music classification
Music can be classified according to higher level tags of the song, such as style, genre, mood, etc.
Classical train/test supervised classification scenario:
MIREX: Classify music into categories
  genre: rock, hip hop, jazz, classical,...
  mood: aggressive, passionate, humorous, cheerful,..
  artist identification
  classical composer identification

## Slide 64: References
Müller, ” Fundamentals of Music Processing”, Springer 2015
Klapuri, Davy, “Signal processing methods for music transcription”, Springer 2006
Judith C. Brown; Calculation of a constant Q spectral transform. J. Acoust. Soc. Am. 1 January 1991; 89 (1): 425–434. https://doi.org/10.1121/1.400476